## Slide 1: Formal Design and Verification of an Asynchronous SRAM Controller
Victor Khomenko, Andrey Mokhov, Danil Sokolov, Alex Yakovlev

## Slide 2: Motivation
SRAM is a ubiquitous component
  so must be robust and efficient
Advantages of asynchronous SRAM:
  reliable operation under a wide range of supply voltages
  can trade off energy for performance (essential for low-power devices, e.g. powered by energy harvesters)
Fascinating challenge for the application of formal models of concurrency!

## Slide 3: Conventional 6T SRAM
Reading: precharge bit-lines, assert WL, sense bit-line changes
Writing: set data lines, assert WL and WE, wait for a while…

## Slide 4: Problem: how long to wait?

## Slide 5: Previous work
Using non-standard memory cells
  Extra transistors, and
  Extra bit-lines or acknowledgement lines
Different delay lines for different voltages
  Voltage references
Duplicating an SRAM line to act as a reference delay line

## Slide 6: Previous work (cont’d)
Async solution with completion detection
  developed by A. Baz et al. (PATMOS 2010, JOLPE 2011) based on the original idea of V. Varshavsky (USSR Patent, 1988)
  no voltage references
  speed-independent, but
  interface to bit-lines is not delay-insensitive
    less robust in the low-power mode, especially if bit-lines are buffered or augmented with a sense amplifier
Completion detection in write mode idea:
  easy when the bit is flipped
  read before writing to check if the bit needs flipping

## Slide 7: Previous work (cont’d)
Hazard due to transient (1,1) on the bit-lines

## Slide 8: Delay models
Delay-insensitive (DI) circuits:
  Both gate delays and wire delays are positive and finite, but variable and unbounded
  Very robust, but there are very few DI circuits
Speed-independent (SI) circuits:
  Gate delays are positive and finite, but variable and unbounded
  Wire delays are negligible (alternatively, wire forks are isochronic)
  OK for small blocks, but inter-block communication may be problematic due to long and/or buffered wires
Compromise:
  SI blocks with DI interfaces

## Slide 9: Specification: top-level structure

## Slide 10: Specification: Master

## Slide 11: Specification: SlaveRead

## Slide 12: Specification: ReadCompletion

## Slide 13: Specification: WriteCompletion

## Slide 14: Simulation results
Only a rough idea
Read cycle (both set and reset phases) is ~3% slower compared to [Baz et al.]
In write mode the overhead is ~11% if the bit-lines flip and ~20% otherwise
Acceptable (?) cost for delay-insensitive interface to bit-lines

## Slide 15: Summary
An alternative to [Baz et al.] design of an asynchronous SRAM controller
  delay-insensitive interface to bit-lines
  performance overhead is small
Systematically designed
Formally verified
The design flow is supported by:
workcraft.org

## Slide 16: Future work
We have ideas how to optimise our design
Fine-tuning the circuit at the transistor and layout levels to push the minimum operating voltage further down
Produce it on silicon to confirm the possibility of reliable operation at sub-threshold voltages

## Slide 17: Thank you! Any questions?